## Slide 1
P31 Grey-Box Approach for Modelling of Converter Interfaced Power Systems
Presented by – Aman, Yash Baghel Roll No. – 220002004, 220002083
EE-493 B.TECH PROJECT End-Semester Evaluation
Department of Electrical Engineering, IIT Indore 21st November 2025
Supervisor: Dr. Lokesh Kumar Dewangan Assistant Professor
1
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 2
Outline
Introduction
  Motivation and Problem Statement
Literature Review
Project Objective
  Main Objective
  Specific Objectives
Methodology
  Frequency Scanning
  Analytical Model
  Vector Fitting
  Component Connection Method
  Stability Assessment
Conclusion and Future Work
2
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 3
Outline
Introduction
  Motivation and Problem Statement
3
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 4
Fast dynamics and low inertia → stability issues.
Multi-vendor converters → limited internal data
Challenges Faced in CIPS
Problem Statement
White-box models: Accurate but need full converter details.
Black-box models: Simple but hide internal states.
Proposed approach: Grey Box Modeling → Uses white box and black box models subsystems and combine them with CCM.
Treat converter as black-box, grid as white-box.
Aim: Efficient and reliable small-signal stability analysis
Fig. 1: Segmented power system for hybrid modelling (white and black model).
Introduction
Motivation and Problem Statement
4
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 5
Outline
Introduction
  Motivation and Problem Statement
Literature Review
5
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 6
Literature Review
Paper | Black-Box Modelling | White-Box Modelling | VF | CCM
Nicolás Cifuentes — “Black-Box Impedance-Based Stability Assessment of Dynamic Interactions Between Converters and Grid,” IEEE Transactions on Power Systems, 2022. |  |  |  | 
Yanbo Wang — “Small-Signal Stability Analysis of Inverter-Fed Power Systems Using Component Connection Method,” IEEE Transactions on Smart Grid, 2018. |  |  |  | 
F. J. Cifuentes Garcia — “Automated Frequency-Domain Small-Signal Stability Analysis of Electrical Energy Hubs,” IEEE ISGT Europe, 2024. |  |  |  | 
L. Reis — “Applying Vector Fitting for Measurement-Based MIMO Model Identification of a Grid-Forming Converter,” IEEE ISGT Europe, 2023 |  |  |  | 
Proposed Method* |  |  |  | 
*Leading Institutions such as DTU, KU Leuven have conducted research aligned with the proposed method
6
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 7
Outline
Introduction
  Motivation and Problem Statement
Literature Review
Project Objective
  Main Objective
  Specific Objectives
7
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 8
To implement a Grey-Box approach for modeling of converter interfaced power systems.
Main Objective
Specific Objectives
To obtain the frequency-domain behavior of a Two-level Voltage Source Converter (VSC) by performing a frequency scan on its PSCAD model.
To apply the Vector Fitting (VF) algorithm to the collected frequency-domain data to derive a continuous state-space model of the VSC
To combine the identified VSC model with an analytical, white-box model of the grid using the Component Connection Method (CCM) to form a complete system representation
To validate the accuracy of the proposed grey-box approach by comparing its results with those obtained from a complete white-box model of the system.
Project Objective
8
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 9
Outline
Introduction
  Motivation and Problem Statement
Literature Review
Project Objective
  Main Objective
  Specific Objectives
Methodology
  Frequency Scanning
  Analytical Model
  Vector Fitting
  Component Connection Method
  Stability Assessment
9
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 10
Methodology
10
Aman and Yash Baghel End-Sem BTP Evaluation
Scanning & Sampling of Black-Box Frequency Response
Vector Fitting of Sampled Response
Open-Loop Model Construction
Define all the differential equations and symbolic variables
Solve for operating point with in-bult solver
Open-Loop Model Construction
Define Studying Frequency Range
System Data Input Available Information
White-Box Subsystem
Black-Box Subsystem
Unified Model Construction
= +
Interaction Mode Identification
Mode Selective Eigenvalue Estimation
Black-Box subsystem
White-Box subsystem
Fig. 2 : Grey Box System Representation

## Slide 11
Frequency scanning techniques (FST) are data-driven methods used to study how a system responds to sinusoidal signals over a range of frequencies.
The corresponding gain and phase shift from FST are plotted as Bode plot to analyse the frequency-domain characteristics of the system.
Fig. 3. Two Level Voltage Source Converter
Methodology
Frequency Scanning
11
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 12
Two Level Voltage Source Converter
Methodology
Fig. 4: Modelling and Control of Two level VSC
12
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 13
Admittance
AC SCAN
FFT
Methodology
13
Aman and Yash Baghel End-Sem BTP Evaluation
Fig. 5 : Direct axis Current and Quadrature axis Current.

## Slide 14
For each frequency , we have:
Magnitude
In decibels (dB):
Phase
Y =
Methodology
Fig. 6: Bode Plots of Frequency Scanning
14
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 15
Methodology
Analytical Model
.
19 differential equations
.
.
This model is derived directly from fundamental differential equations using known system physics.
Fig. 7: Modelling and Control of Two level VSC
15
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 16
Methodology
Results
Fig. 8: Bode Plots of Frequency Scanning (dashed) and Analytical Model (Solid)
16
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 17
Methodology
Vector Fitting
Fig. 9: Converting Bode Plot data to State Space Model
17
Aman and Yash Baghel End-Sem BTP Evaluation
Subsystem-1
Subsystem-2
Subsystem-3

## Slide 18
Methodology
Vector Fitting
Start: Frequency-domain data (s, H(s))
Choose initial poles (linear/log spaced or user input)
Form auxiliary equation with scaling function σ(s)
Update poles: new poles = zeros of σ(s)
Solve linear least squares for residues,
Check convergence (pole movement, error reduction)
Final residues + asymptotic terms
Construct final model: Pole-residue form, State-space form
Convergence achieved?
Yes
No
+
(1)
(2)
(3)
(4)
18
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 19
Methodology
Results
Bode Plot
Eigenvalue Plot
Fig. 10: Free and Relaxed vector fitting results
Fig. 11: Eigenvalues Plot
19
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 20
Methodology
Component Connection Method
The component connection method (CCM) easily composes small-signal models from subsystems in state-space, which can be used for eigenvalue based and impedance-based stability assessment.
where,
Fig. 12: Combined State space Model
20
Aman and Yash Baghel End-Sem BTP Evaluation
Subsystem-1
Subsystem-2
Subsystem-4
Subsystem-3
Here, are the component of interconnection matrix.

## Slide 21
Methodology
Stability Assessment
Computation efficient gray-box approach for stability assessment
21
Aman and Yash Baghel End-Sem BTP Evaluation
Divide in Subsystems
Subsystem SSM
Obtain open loop eigenvalues
Identify interacting eigenvalues
Obtain closed loop eigenvalues with the help of coupling gain
(2)
(1)

## Slide 22
Methodology
Results
22
Aman and Yash Baghel End-Sem BTP Evaluation
Fig. 13: Closed loop eigenvalue estimation

## Slide 23
Outline
Introduction
  Motivation and Problem Statement
Literature Review
Project Objective
  Main Objective
  Specific Objectives
Methodology
  Frequency Scanning
  Analytical Model
  Vector Fitting
  Component Connection Method
  Stability Assessment
Conclusion and Future Work
23
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 24
Conclusion and Future Work
Conclusion
We developed a novel Grey-Box modeling method that combines frequency-domain black-box identification with analytical white-box grid modeling through the Component Connection Method (CCM).
The approach eliminates the need for detailed vendor-specific converter parameters.
The unified Grey-Box model enabled efficient eigenvalue-based stability assessment.
Overall, the proposed method bridges the gap between full white-box accuracy and black-box practicality while maintaining computational efficiency.
Future Work
Extend the proposed method to Multi-terminal HVDC system, which includes MMCs.
We are currently working on preparing a journal paper based on the same methodology.
24
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 25
Thanks for your attention!
Aman, Yash Baghel
ee220002004@iiti.ac.in, ee220002083@iiti.ac.in
Questions?
25
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 26
VF approximates the frequency response data with a high-order rational function.
Appendix - 1
Vector Fitting
26
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 27
Admittance
Appendix-2
FFT
The Fast Fourier Transform (FFT) is an efficient O(NlogN) algorithm for calculating DFTs. The Fourier Transform converts a signal from its original domain (often time or space) to a representation in the frequency domain and vice versa.
k is the frequency index
27
Aman and Yash Baghel End-Sem BTP Evaluation

## Slide 28
28
Aman and Yash Baghel End-Sem BTP Evaluation
Appendix-3
Fig. : Flowchart of PEDIM